## Slide 1: Control System Miniseries
05/15/2012

## Slide 2: Lecture 1
What is control system
Control system diagram and terminology
Mathematic relations.

## Slide 3: What Is Control System
A control system is a device, or set of devices to manage, command, direct or regulate the behavior of other devices or system. – From Wikipedia.
  Feed forward (open loop) control
    Shooter tester
  Feedback (close loop) control
    Shooter with hall effect speed sensor

## Slide 4: Feed Forward Control
Controller
Plant
Input
Output
Control Variable
C
P
Xcmd
Xctrl
Xout
Plant – a physical system to be controlled; robot driving base, shooter wheel
Input – Target/desired value of plant output; robot position, shooter speed, joystick input counts
Controller – signal converter, conditioner;
Control Variables – Physical signal which plant can take as input; voltage, torque
Output – Physical response of plant to its input.
In time domain:
Xctrl (t) = C(Xcmd, t)
Xout (t) = P(Xctrl, t),
For a linear system and in frequency domain:
Xctrl (s) = C(s)Xcmd(s)
Xout (s) = P(s) Xctrl(s) = P(s) C(s) Xcmd(s)
s = jω = j(2πf), f - frequency

## Slide 5: Feedback Control System
Controller
Plant
Input
Output
Control Variable
Sensor
+
-
Error
C
P
S
+
-
Err
Xcmd
Xctrl
Xout
In time domain:
Xfbk(t) = S(Xout, t)
Err(t) = Xcmd(t) – Xfbk(t)
Xctrl (t) = C(Err, t)
Xout (t) = P(Xctrl, t),
For a linear system and in frequency domain:
Xfbk(s) = S(s) Xout (s)
E(s) = Xcmd(s) – Xfbk(s)
Xctrl (s) = C(s) E(s) = C(s) [Xcmd(s) - Xout (s)]
Xout (s) = P(s) Xctrl(s) = P(s) C(s) [Xcmd(s) - Xout (s)]
Xout (s) = {P(s)C(s) /[1 + P(s) C(s) S(s)]} Xcmd(s)
Xfbk
Feedback

## Slide 6: Example
Shooter Wheel
Calculated Wheel Speed
Wheel
Speed
Hall Effect Sensor
(Voltage Pulse Generator
+
-
Speed Error
ω0
(rpm)
Gearbox
Motor
Jaguar
Speed Controller
Control Software
Pulse Counter
Voltage to Speed Converter
Δω
(rpm)
Vctrl (volt)
Vm
(volt)
Tm
(N-m)
Tgb
(N-m)
ωwhl
(rpm)
Control Voltage
Motor Voltage
Motor Output Torque
Gearbox Output Torque
Voltage of Pulse Rate
Pwhl
(# of pulse)
Vpls
(volt)
ωfbk
(rpm)
Sensor Pulse
Measured Wheel Speed
Controller
Plant
Sensor
Present every major component
Label variables and physical unit
Label conversion factor

## Slide 7: Summary
Major control system include
  plant, controller and sensor blocks
Each block contains many physical components.
Present physical components with input and output variables.
Establish math function between input and output of each component with proper unit.

## Slide 8: Homework (two weeks)
Find the conversion factors for each box of shooter control diagram (analytical, experimental, or online search).
Write done the algorithm (logic steps) of current version of control SW.
Advanced home work
  What is block diagram (mathematic relation) of a motor?
  Is Jaguar a simple proportional components?
  Besides driving torque, are there any other torques acting on shooter wheel?

## Slide 9: Make a Test Fixture for Lecture 2
Dip weight ball or a rod into liquid.
Suddenly lift top end of spring a distance.
Observe weight movement.
Thinner liquid
Thicker liquid
Container
Weight (ball)
Spring
Find a spring and weight
Make resonator about a couple to a few Hertz.
Make different thickness (viscosity) liquid out of powder material.
Indicator