## Slide 1: Control System Miniseries - Lecture 4
06/11/2012

## Slide 2: Lecture 4 Basic Math/Physics Concepts Used in System Modeling
Math
  Difference, Difference Quotient & Derivative
  Summation & Integration
Physics
  Force analysis – free body diagram
  Newton’s Laws
  Acceleration, velocity and displacement
Block Diagram Operation
  Transfer function
Note: In this lecture, we bring advance concepts to in a simple and understandable way. As long as you read the material carefully, for most contents, you have no problem to understand them.

## Slide 3: Outline – A Point Motion
Linear Motion of a Point
  Position and Displacement of a Point
  Velocity of a Point
  Acceleration of a Point
Angular Motion of a Point
  Angular Position and Displacement of a Point
  Angular Velocity of a Point
  Angular Acceleration of a Point

## Slide 4: Position and Displacement of a Point
Position
  Position is coordinates of a point in a coordinate system (1D, 2D, or 3D)
Displacement
  Displacement is position difference between a point and another point.
  ΔXBA = XB – XA
  Different from distance, displacement has direction.
  Unit: m (or mm, inch, feet, etc.)
X (m)
XA
XB
-1
0
1
2
-2
3
A
B
C
XC
Example:
An object moves to B position from A position
Then, move to C from B.
Point | Position | Motion | Displacement
A | XA = 1 m |  | 
B | XB = 3 m | A -> B | ΔXBA = XB – XA = 3 m – 1 m = 2 m
C | XC = -2 | B -> C | ΔXCB = XC – XB = -2 m – 3 m = -5 m

## Slide 5: Angular Position and Displacement of a Point
Angular Position
  Angular position is angular coordinates of a point in a coordinate system (2D, or 3D)
Angular Displacement
  Angular displacement is angular position difference between a point and another point.
  ΔθBA = θB – θA
  Angular displacement has direction.
  Unit: Radian (or degree)
Example:
An object rotates to B position from A position
Then, rotates to C from B.
A (θA = π/3 Rad)
B (θB = 2π/3 Rad)
C (θC = -π/4 Rad)
Point | Position | Motion | Displacement
A | θA = π/3 Rad |  | 
B | θB = 2π/3 Rad | A -> B | ΔθBA = θB – θA = 2π/3 Rad – π/3 Rad = π/3 Rad
C | θC = -π/4 Rad | B -> C | ΔθCB = θC – θB = -π/4 Rad– 2π/3 Rad = -11π/2 Rad

## Slide 6: Velocity – Linear Motion of a Point
Velocity
  Velocity is measurement of how fast a object moves.
    Average velocity: ratio of displacement (ΔX) to time change (Δt) during which displacement takes place.
    Vavg = ΔX/ Δt
    Instantaneous Velocity: rate of displacement change at time, which is derivative of displacement w.r.t. time. (For derivative, please see slide later.)
    V = dX/dt
  Unit: m/s (or mm/s, ft/s, etc.)
Example:
An object takes 2 sec to move from position A to B,
Then it takes 2.5 sec to move from B to C
 | Displace-ment | Time Change | Average Velocity
A -> B | ΔXBA=2 m | ΔtAB = 2 s | VAB = ΔXBA/ΔtAB = 2 m/2 s = 1 m/s
B -> C | ΔXCB= -5 m | ΔtBC = 2.5 s | VBC = ΔXCB/ΔtBC = -5 m/2 s = -2.5 m/s
X (m)
XA
XB
-1
0
1
2
-2
3
A
B
C
XC

## Slide 7: Angular Velocity – Rotation Motion of a Point
Angular velocity
  Angular velocity is measurement of how fast a point rotates about a fixed point.
    Average angular velocity: ratio of angular displacement (Δθ) to time change (Δt) during which angular displacement takes place.
    ωavg = Δθ/ Δt
    Instantaneous angular velocity: rate of angular displacement change at time, which is derivative of displacement w.r.t. time. (For derivative, please see slide later.)
    ω = dθ/dt
    Velocity has direction.
    Unit: rad/s (or deg/s, rpm, etc)
Example:
An object takes 2 sec to move from position A to B,
Then it takes 2.5 sec to move from B to C
Motion | Angular Displacement | Time Change | Angular Velocity
A -> B | ΔθBA = π/3 Rad | ΔtAB = 2 s | ωAB = ΔθBA/ΔtAB = 2 Rad/2 s = 1 rad/s
B -> C | ΔθCB = -11π/2 Rad | ΔtBC = 2 s | ωBC = ΔθCB/ΔtBC = -5 Rad/2 s = -2.5 Rad/s
A (θA = π/3 Rad)
B (θB = 2π/3 Rad)
C (θC = -π/4 Rad)

## Slide 8: Acceleration – Linear Motion of a Point
Acceleration
  Acceleration is measurement of how fast velocity changes.
    Average acceleration: ratio of velocity changes (ΔV) to time change (Δt) which velocity change takes place
    aavg= ΔV/ Δt
    Instantaneous Acceleration: Rate of velocity change at time, which is derivative of velocity w.r.t. time. For derivative, please see slide later.
    Acceleration has direction
    Unit: m/s2 (or ft/s2, g, etc.)
Example:
An object takes 2 sec to move from position A to B,
Then it takes 2.5 sec to move from B to C
 | Velocity Change | Time Change | Average Acceleration
A -> B | ΔVBA=VB-VA =2 m/s – 0 =2 m/s | ΔtAB = 2 s | aAB = ΔVBA/ΔtAB = 2 m/s/2 s = 1 m/s2
B -> C | ΔVCB=VC-VB =-2 m/s –2 m/s = -4 m/s | ΔtBC = 2 s | aBC = ΔVCB/ΔtBC = -4 m/s/2 s = -2 m/s2
X (m)
XA
XB
-1
0
1
2
-2
3
A
B
C
XC
VA= 0
VB = 2 m/s
VC = - 2 m/s

## Slide 9: Angular Acceleration – Rotation Motion of a Point
Angular acceleration
  Angular acceleration is measurement of how fast angular velocity changes about a fixed point.
    Average angular acceleration: ratio of angular velocity changes (Δω) to time change (Δt) which angular velocity change takes place.
    εavg= Δω / Δt
    Instantaneous Acceleration: Rate of velocity change at time, which is derivative of velocity w.r.t. time. For derivative, please see slide later.
    ε= dω/dt
    Angular acceleration has direction.
    Unit: rad/s2
 | Angular Vel. Change | Time Change | Average Acceleration
A -> B | ΔωBA=ωB-ωA =2 Rad/s – 0 =2 Rad/s | ΔtAB = 2 s | εAB = ΔωBA/ΔtAB = 2 Rad/s/2 s = 1 Rad/s2
B -> C | ΔωCB=ωC-ωB =-2 Rad/s –2 Rad/s = -4 Rad/s | ΔtBC = 2 s | εBC = ΔωCB/ΔtBC = -4 Rad/s/2 s = -2 Rad/s2
Example:
An object takes 2 sec to rotate from position A to B,
Then it takes 2.5 sec to rotate from B to C
A (θA = π/3 Rad)
B (θB = 2π/3 Rad)
C (θC = -π/4 Rad)

## Slide 10: Summary
Point | Position | Instantaneous Velocity | Time | Motion | Time Change | Displacement | Velocity Change | Average Velocity | Average Acceleration
A | XA = 1 m | VA = 0 | tA = 0 |  |  |  |  |  | 
B | XB = 3 m | VB = 2 m/s | tB = 2 s | A -> B | ΔtAB = 2 s | ΔXBA = XB –XA = 2 m | ΔVBA=VB-VA =2 m/s | VAB = ΔXBA/ΔtAB = 1 m/s | aAB = ΔVBA/ΔtAB = 1 m/s2
C | XC =-2 m | VC = -2 m/s | tC = 4 s | B -> C | ΔtBC = 2 s | ΔXCB =XC – XB = -5 m | ΔVCB=VC-VB = -4 m/s | VBC = ΔXCB/ΔtBC = -2.5 m/s | aBC = ΔVCB/ΔtBC = -2 m/s2
X (m)
XA
XB
-1
0
1
2
-2
3
A
B
C
XC
VA= 0
VB = 2 m/s
VC = - 2 m/s
tC = 4 s
tA = 0 s
tB = 2 s

## Slide 11: Summary
Point | Position | Instantaneous Velocity | Time | Motion | Time Change | Displacement | Velocity Change | Average Velocity | Average Acceleration
A | XA = 1 m | VA = 0 | tA = 0 |  |  |  |  |  | 
B | XB = 3 m | VB = 2 m/s | tB = 2 s | A -> B | ΔtAB = 2 s | ΔXBA = XB –XA = 2 m | ΔVBA=VB-VA =2 m/s | VAB = ΔXBA/ΔtAB = 1 m/s | aAB = ΔVBA/ΔtAB = 1 m/s2
C | XC =-2 m | VC = -2 m/s | tC = 4 s | B -> C | ΔtBC = 2 s | ΔXCB =XC – XB = -5 m | ΔVCB=VC-VB = -4 m/s | VBC = ΔXCB/ΔtBC = -2.5 m/s | aBC = ΔVCB/ΔtBC = -2 m/s2
A, θA = π/3 Rad,
B, θB = 2π/3 Rad,
C, θC = -π/4 Rad

## Slide 12: Appendix: Derivative and Integration
Derivative is the rate of changes of one variable with respect to another.
  Rate is ratio when the changes of relevant variables are infinitesimal.
  For a number of frequently used functions, derivative can be calculated by following simple three steps
    Difference
    Difference Quotient
    Derivative
Simply speaking, integration is summation.
  However, its exact definition can not be simply described because there are two types of integration
    Definitive integration
    In-definitive integration
  Integration of a couple of function can be demonstrated with approximation of summation. Integration of other functions needs more math preparation.
  However, in-definitive integration is reverse calculation of derivative. So, we take short cut to calculate integration by knowing original function of a derivative.

## Slide 13: Derivative
Derivative is the rate of changes of one variable with respect to another.
Example 1
  At lower gear, a robot moves forward 6 ft within 1 sec, (6 ft – 0 ft)/(1 sec – 0 sec)= 6 ft/sec
  At higher gear, it moves 16 ft within 1 sec, (16 ft – 0 ft)/(1 sec – 0 sec) = 16 ft/sec
  The derivative in this case is the rate of change of distance with respect to time, called speed in physics.
Example 2
  Drive train with one CIM motor per gear box can speed up robot to 16 ft/sec within 2 sec, (16 ft/sec – 0 ft/sec)/(2 sec) or 8 ft/sec2
  Drive train with two CIM motors per gear box can speed up robot to 16 ft/sec within 1 sec, (16 ft/sec – 0 ft/sec)/sec or 16 ft/sec2
  The derivative in this case is the rate of change of speed with respect to time, called acceleration in physics.
Slide x shows a three steps approach to calculate derivative in general

## Slide 14: Integration
Simply speaking, integration is summation.
Example 1
  A robot moves at 1 ft/sec speed. Over 10 sec, this robot will move 10 ft, (1 ft + 1 ft + … + 1 ft) =10 ft.
Example 2
  A robot average speed is 1 ft/sec at 1st sec, 2 ft/sec at 2nd sec, 3 ft/sec at 3rd sec,…, etc. Basically, it is speeding up (accelerates). 5 sec later, this robot speed will reach

## Slide 15: Difference, Difference Quotient & Derivative
Difference
  Draw a straight line through point A and B of function y = f(x), Δx and Δy is the difference in X and Y axis between point A and B.
Difference Quotient
  The difference quotient is
Derivative
  If move point B toward point A (reduce Δx), the straight line AB will approach to tangent line of function y = f(x) at point A.
  When Δx is infinitesimal (Δx => 0), the difference quotient
  becomes derivative and denoted as.
Following above simple steps, we can derive a few frequently used derivatives. See next slide.
x1
x2 = x1 + Δx
y1 = f(x1)
y2 = f(x2)
Δx
Δy
X
Y
A
B
xi
xi+1 = xi + Δx
yi = f(xi)
yi+1 = f(xi+1)
Δx
Δy
X
Y
A
B
y = f(x)

## Slide 16: Frequently Used Derivatives - There are more derivative can be derived by following same steps as below
If y = f(x) = C ( a constant), dy/dx =0
If y = f(x) = xn , n /= 0, then, dy/dx = n xn-1
If y = f(x) = sin x (or cos x), dy/dx = cos x (or -sin x)
If y = f(x) = kx, then, dy/dx = k

## Slide 17: More about Derivative
If x is time t, derivative can be expressed in following form
If taking derivative to derivative , we get second derivative and noted as
Again, if x is time t, second derivative is expressed as
In physics, if distance s is function of time t, s = f(t), the first derivative of s with respect to time t is velocity, and denoted as
Also, first derivative of velocity v with respect to t is acceleration
Because acceleration is second derivative of distance s, so

## Slide 18: Application
If an object move can be expressed with function x = f(t) = 1/2gt^2, what is its velocity and acceleration.
Velocity is 1st derivative of distance with respect to time t
  V = dx/dt = d(1/2gt^2)/dt = 1/2gd(t^2)/dt = g*t.
  Velocity linearly increases with respect to time.
  Other expression of velocity
    V = x’ or v = x
Acceleration is the 1st derivative of velocity, or 2nd derivative of distance with respect to time t. So,
  A = dV/dt = d(gt)/dt =g dt/dt = g
  Acceleration is constant g
  Other expression of acceleration
    A = v’ = s’’or A = v = x
This is distance (s), velocity (v = gt) and acceleration (a = g) of free fall object

## Slide 19: Area, Summation, Integral
Area I and Definitive Integration
  Area I is in blue color under function y = f(x)
  Calculate this area is called definitive integration of y = f(x) from x1 (=a) and to xn (=x).
Summation
  Area I can be estimated by summation of small rectangle area yi*Δx.
Integration
  When Δx is infinitesimal (Δx => 0), the estimated Area will be equal to Area I.
x1=a
xn = x
y1 = f(x1)
yn = f(xn)
X
Y
y = f(x)
…
y2 = f(x2)
Area I
x1=a
xn = x
y1 = f(x1)
yn = f(xn)
X
y = f(x)
…
y2 = f(x2)
x2
Δx
Δx
Δx

## Slide 20: Examples of Simple Integration
Example 1
  Function: y = f(x) = k (constant)
  Integration: Area = k*(x – x0) = kx – kx0 = kx + C
Example 2
  Function: y = f(x) = 2ax
  Integration: Area = (2ax0 + 2ax)(x-x0)/2 =ax^2 – ax1^2
  = ax^2 + C
Above integration results of a function equal a variable term + a constant.
  This is true for most integration.
  The variable part is called in-definitive integration
So
x1=a
xn = x
y1 = f(x1)
yn = f(xn)
X
Y
y = f(x)
y2 = f(x2)

## Slide 21: Relationship between Derivative and Indefinite Integration

## Slide 22: Core Contents of Lecture 1
Drawing a system block diagram is starting point of any control system design.
  Example, ball shooter of 2012 robot
Shooter Wheel
Wheel
Speed
Hall Effect Sensor
(Voltage Pulse Generator
+
-
Speed Error
ω0
(rpm)
Gearbox
Motor
Jaguar
Speed Controller
Control Software
Pulse Counter
Voltage to Speed Converter
Δω
(rpm)
Vctrl (volt)
Vm
(volt)
Tm
(N-m)
Tgb
(N-m)
ωwhl
(rpm)
Control Voltage
Motor Voltage
Motor Output Torque
Gearbox Output Torque
Voltage of Pulse Rate
Pwhl
(# of pulse)
Vpls
(volt)
ωfbk
(rpm)
Sensor Pulse
Measured Wheel Speed
Controller
Plant
Sensor
Tip: Draw a system block diagram
On our robot, starting from shooter wheel, you can find a component connecting to another component. For example, wheel is driven by gearbox, gearbox is driven by a motor, motor is driven by speed controller, …. Physically you can see and touch most of them on our robot.
For each component, draw a block in system diagram.
Name input and output of each block, present them in symbols. Later, you will use these symbols to present mathematic relation of each block and entire system.
Define unit of each variable (symbol)
Notes: Lecture 1 briefly tell us what is control system. But, the core content is how to present a system in block diagram.
After you have completed the diagram, you are ready to analyze individual blocks, then the whole system

## Slide 23: Core Contents of Lecture 2
To a step input (the red curve in following plots), responses of system with a well designed controller should have performance as the green curves.
  Green curves in both plots have optimal damping ratio (0.5 ~ 1)
  But, the green curve in right figure is preferred because it has faster response (higher bandwidth)
Systems with behavior as shown in above figures can be represented by 2nd order differential equation.
Tip: We take an approach to design our control system without solving this differential equation.
  Model robot system based on physics and mathematics.
  Typically we will get the 2nd order differential equation as above. Then we optimize
    Damping ratio: ζ = 0.5 ~ 1.
    System bandwidth(close loop): ωb = 5 - 10 Hz for 50 Hz control system sampling rate
Notes: Before getting on road, you should know your destination, meaning what is targeted system performance.
Optimal-damping and higher close loop bandwidth is destination of control system design.
Optimizing ζ and ωb will be much easier job because you will just solve simple algebra or trigonometry.
    We will show you, through rest of lecture, how generate 2nd order differential equation and extract ζ and ωb .

## Slide 24: Core Contents of Lecture 3
The characteristics of 2nd order differential equation (or a system which can be presented by the same equation)
can be examined by solving special cases such as F(t) = 0 or F(t) = 1 and given initial conditions.
  At this point, you can use solutions from Mr. G’s presentation for our robot control system analysis and design.
  Tip: use published solutions listed in table below for your simulation.
Notes: Solutions for a 2nd order differential equation depend on input function of F(t) and system initial conditions.
  Complete solution is out of scope of mini lecture. You will have opportunities to understand how to solve differential equations in college.

## Slide 25: Heads-up
In rest of lectures we will get on real stuff of our robot.
First, we will model ball shooter wheel, its gearbox and motor, etc.
Second, analyze a proportional controller.
  Proportion controller (P)with speed feedback is used on our shooter.
  Answer why the system is always stable (thinking about damping). Can step response be faster?
  Run step response test.
  Answer why this system can not keep constant speed in SVR. We will introduce disturbance input in block diagram.
Third, we will change the controller to proportion – integration controller (PI)
  Analyze that under which condition this system will be stable or not stable.
  Program the controller on robot and see step response.
  Add load to shooter and see if speed can be constant.
Fourth, we will change the controller to proportion-integration-derivative (PID) controller if we can not achieve stable operation from above design.
  Modeling and analysis could be more complicated for students. But we will give a try.
  We will finalize the design and tune the system for CalGame.
Then, we will get on aiming position control system design for CalGame.